## Slide 1: A Practical Introduction to Crocoddyl
17.03.2020 Julian Eßer

## Slide 2: Overview
Introduction
Workflow & Example
Modeling Bipedal Walking
Preliminary Results with RH5

## Slide 4: Introduction
Optimal Control library for contact sequences
Input: Single/multi-shooting problem
Output: Optimal trajectories & control policy
DDP based optimal control solvers
C++ library with python bindings
Dependencies:
  Pinocchio (dynamics + analytical derivatives)
  Gepetto (3D visualization)

## Slide 5: Introduction
Focus on multi-contact optimal control problems
Terminal knot
Running knots
Goal:
Optimal Trajectories +
Optimal Control Inputs
{Input torques, contact forces}
Notes: Reduce complexity: Not searching for optimum for all x, but for defined initial configuration x0 (reduce complexity)
Control u=(tau,lambda): Input torques+contact forces
Subject to system dynamics

## Slide 6: Workflow
Load robot model
For each knot: Define action model
Add differentiation/integration routines
Setup shooting problem
Apply solver
Action Model :=
{Dynamics + Costs} for one knot
Shooting Problem :=
{N Running Models + Terminal Model}
Notes: 1. URDF, SRDF, Meshes

## Slide 7: Action Model: Components
Current State
Cost Model
  State/Control
  Frame displacements
  CoM/CMP
Contact Model
  3D/6D contact Jacobians

## Slide 8: Example: Goal Reaching with Robotic Arm

## Slide 9: Modeling Bipedal Walking
Parameterize contact sequence
Define shooting problem - Locomotion phases:
Create individual action models
  6D multi-contact model
  Cost model (CoM & foot tracking, friction cone, state, control)
  Differential & Integration Rules
(Pseudo-) Impulse model
1. Double Support
2. Right Step
3. Double Support
4. Left Step

## Slide 10: Preliminary Results with RH5
Integrating a simple model
Performing a full gait
Notes: Model: Serial model of the RH5 legs

## Slide 11: RH5 Analysis: Bounded Input Torques
URDF joint limits
Joint limits reduced by 50 percent

## Slide 12: RH5 Analysis: Varying Gait Phases

## Slide 13: RH5 Analysis: Talos vs. RH5

## Slide 14: RH5 Analysis: Init Pose Variants
„Sitting“ position
Init near zero configuration
Init at zero configuration

## Slide 15: RH5 Analysis: State Periodicity
Approach: Penalize state variations
Next idea: Eq-constrain for terminal state

## Slide 16: RH5 Analysis: Legs + Torso

## Slide 17: RH5 Analysis: Stabilizing the Torso

## Slide 18: Lessons Learned
With Crocoddyl
  Installation through robotpkg manager (not from source)
  Still under development
With RH5
  Basic walking patterns worked
  Range of motion seems useful
Further Investigations
  Real world: First (offline computed) experiments
  Simulation: Towards highly dynamic movements

## Slide 19: Related Links
Project Documentation:
https://github.com/julesser/oc-frameworks
RH5 Results:
https://github.com/julesser/crocoddyl/tree/devel/examples
RH5 Models:
https://git.hb.dfki.de/jesser/abstract-urdf
Crocoddyl Paper:
https://arxiv.org/pdf/1909.04947.pdf
Crocoddyl Video:
https://www.youtube.com/watch?v=wHy8YAHwj-M
Bipedal Walking with the Talos Robot:
https://hal.archives-ouvertes.fr/hal-02383130/document